## Slide 1: A practical approach of IoRT
Presented by
Gerardo Martino
Silvio Di Martino
Computer Science – Internet of Things
Lab of IoT
Notes: Good evening everyone, I am Gerardo and today il will present a practical approach of IoRT an architecture able to detect and object in a workspace and by using a robotic arm pick and place that object in a specific location in order to be recognized.

## Slide 2: INTRODUCTION
I.
Notes: Lets start by introducing few concept

## Slide 3: Introduction
A 6DOF + gripper robotics arm
IoT and Robotics = IoRT
A warehouse management system with 3 different sorting paths
An architecture supporting interaction between sensing devices and robotics arm
A smart car equipped with a camera
Notes: - In industrial and automatic sector the integration between IoT and IIoT ha enable what is called IoRT.
- The term IoRT denotes a concept where data from sensors and other sources are merged in order to create an intelligent system, able to perform a specific task.
The aim of the project is to have a 6DOF (degree of freedom) robotic arm, able to peak and place an object in front of the camera and be recognized.
Also a way to control the robotic arm manually through web control panel.
Therefore it is necessary to create an architecture that supports the interaction of all the nodes (robotics arm, detection and localization and object recognition nodes).

## Slide 4: HARDWARE
II.

## Slide 5: List of Components
Raspberry Pi
01
It’s a small, powerful and cheap computer board. The model used in this project is the 3B with Wi-Fi module integrated on board. Raspbian in the OS in use, and one of the great thigs about the board is that it has a wide range of usage.
Notes: So, thw main components used in this project are:
The RaspberryPi that is a small computer in this project I used the one integrated with WIFI module, it support most of the I/O peripherals. The OS is Linux base and it Raspbian.
At point two we have 3xMCU ESP32, the module can be easily programmed via Arduino IDE, after installing the EPS32 board in the board manager.
They are particularly used for IoT application because they integrate a WIFI and Bluetooth modules. They operate at 2.4GHz with a date transmission rate about 150Mbps. The board has several digital and analog pins, that help to make great prototype. One of the ESP32 is integrated with camera and it is used to stream and capture the image from the browser.
Il module PWM with 16 output channel is mainly used to control LED and servo motor. For this project it used as a simple external power supply at 6V.
The ultrasound sensor and the PRI motion sensor are used as proximity sense, the first measure the distance between sensor and object the second it is used to sense the movement surrounding the environment.
With These two sensor we can simulate a object detection and localization system.
Finally we have the servo that allow us to move the robotic arm, with rotation range of 0 to 180 degree. It is used mostly for remote control and as joint for the robotic arm.

## Slide 6: List of Components
Battery litio
Arduino uno rev2
Robot car kit
IR KY-032
03
DC Motor
04
It is an infrared sensor used for the detection of obstacles, as it is equipped with an IR emitter and an IR receiver that allow Arduino to signal the presence of objects in the range of this sensor.
Arduino UNO WiFi Rev.2 is the one-stop-solution for many of the basic IoT application scenarios.
1x Arduino Rev2
02
Battery kit
05
Notes: So, thw main components used in this project are:
The RaspberryPi that is a small computer in this project I used the one integrated with WIFI module, it support most of the I/O peripherals. The OS is Linux base and it Raspbian.
At point two we have 3xMCU ESP32, the module can be easily programmed via Arduino IDE, after installing the EPS32 board in the board manager.
They are particularly used for IoT application because they integrate a WIFI and Bluetooth modules. They operate at 2.4GHz with a date transmission rate about 150Mbps. The board has several digital and analog pins, that help to make great prototype. One of the ESP32 is integrated with camera and it is used to stream and capture the image from the browser.
Il module PWM with 16 output channel is mainly used to control LED and servo motor. For this project it used as a simple external power supply at 6V.
The ultrasound sensor and the PRI motion sensor are used as proximity sense, the first measure the distance between sensor and object the second it is used to sense the movement surrounding the environment.
With These two sensor we can simulate a object detection and localization system.
Finally we have the servo that allow us to move the robotic arm, with rotation range of 0 to 180 degree. It is used mostly for remote control and as joint for the robotic arm.

## Slide 7: List of Components
6x Servo MG996R
07
PCA9685 I2C Control
08
It is a motor that can be turned to a specified position, from 0 to 180 degree. It is used in remote control (RC) world and also for robotics and automation projects.
It is a 16 PWM output channel mainly used to control LEDs, but it can be used also to control servos or as power supply at 6V.
The robot skeleton.
Robot chassis kit
06
Notes: So, thw main components used in this project are:
The RaspberryPi that is a small computer in this project I used the one integrated with WIFI module, it support most of the I/O peripherals. The OS is Linux base and it Raspbian.
At point two we have 3xMCU ESP32, the module can be easily programmed via Arduino IDE, after installing the EPS32 board in the board manager.
They are particularly used for IoT application because they integrate a WIFI and Bluetooth modules. They operate at 2.4GHz with a date transmission rate about 150Mbps. The board has several digital and analog pins, that help to make great prototype. One of the ESP32 is integrated with camera and it is used to stream and capture the image from the browser.
Il module PWM with 16 output channel is mainly used to control LED and servo motor. For this project it used as a simple external power supply at 6V.
The ultrasound sensor and the PRI motion sensor are used as proximity sense, the first measure the distance between sensor and object the second it is used to sense the movement surrounding the environment.
With These two sensor we can simulate a object detection and localization system.
Finally we have the servo that allow us to move the robotic arm, with rotation range of 0 to 180 degree. It is used mostly for remote control and as joint for the robotic arm.

## Slide 8: List of Components
1x ESP32 Cam
10
4x DC Motor
11
It is an infrared sensor used for the detection of obstacles, as it is equipped with an IR emitter and an IR receiver that allow Arduino to signal the presence of objects in the range of this sensor.
Arduino UNO WiFi Rev.2 is the one-stop-solution for many of the basic IoT application scenarios.
1x Arduino Rev2
09
Car and battery kit
12
Notes: So, thw main components used in this project are:
The RaspberryPi that is a small computer in this project I used the one integrated with WIFI module, it support most of the I/O peripherals. The OS is Linux base and it Raspbian.
At point two we have 3xMCU ESP32, the module can be easily programmed via Arduino IDE, after installing the EPS32 board in the board manager.
They are particularly used for IoT application because they integrate a WIFI and Bluetooth modules. They operate at 2.4GHz with a date transmission rate about 150Mbps. The board has several digital and analog pins, that help to make great prototype. One of the ESP32 is integrated with camera and it is used to stream and capture the image from the browser.
Il module PWM with 16 output channel is mainly used to control LED and servo motor. For this project it used as a simple external power supply at 6V.
The ultrasound sensor and the PRI motion sensor are used as proximity sense, the first measure the distance between sensor and object the second it is used to sense the movement surrounding the environment.
With These two sensor we can simulate a object detection and localization system.
Finally we have the servo that allow us to move the robotic arm, with rotation range of 0 to 180 degree. It is used mostly for remote control and as joint for the robotic arm.

## Slide 9: List of Components
Raspberry Pi
01
IR KY-032
04
ESP32 CAM
05
DC Motor
06
It’s a small, powerful and cheap computer board. The model used in this project is the 3B with Wi-Fi module integrated on board. Raspbian in the OS in use, and one of the great thigs about the board is that it has a wide range of usage.
Servo MG996R
02
PCA9685 I2C Control
03
It is a motor that can be turned to a specified position, from 0 to 180 degree. It is used in remote control (RC) world and also for robotics and automation projects.
It is a 16 PWM output channel mainly used to control LEDs, but it can be used also to control servos or as power supply at 6V.
It is an infrared sensor used for the detection of obstacles, as it is equipped with an IR emitter and an IR receiver that allow Arduino to signal the presence of objects in the range of this sensor.
ESP32 is used for a variety of IoT applications, because of the WiFi and BLE module integrated. The WiFi protocol operates at 2.4 GHz with a data rate up to 150 Mbps. It is a MCU with multiple digital and analog I/O pins to connect sensing or actuation devices.
It is a motor that combined with the wheels lets the car move.
Battery litio
2xArduino uno rev2
2xSmart car shield
Robot arm kit
Robot car kit
Notes: So, thw main components used in this project are:
The RaspberryPi that is a small computer in this project I used the one integrated with WIFI module, it support most of the I/O peripherals. The OS is Linux base and it Raspbian.
At point two we have 3xMCU ESP32, the module can be easily programmed via Arduino IDE, after installing the EPS32 board in the board manager.
They are particularly used for IoT application because they integrate a WIFI and Bluetooth modules. They operate at 2.4GHz with a date transmission rate about 150Mbps. The board has several digital and analog pins, that help to make great prototype. One of the ESP32 is integrated with camera and it is used to stream and capture the image from the browser.
Il module PWM with 16 output channel is mainly used to control LED and servo motor. For this project it used as a simple external power supply at 6V.
The ultrasound sensor and the PRI motion sensor are used as proximity sense, the first measure the distance between sensor and object the second it is used to sense the movement surrounding the environment.
With These two sensor we can simulate a object detection and localization system.
Finally we have the servo that allow us to move the robotic arm, with rotation range of 0 to 180 degree. It is used mostly for remote control and as joint for the robotic arm.

## Slide 10
Hardware Connection
Conveyor belt
Smart car
Robot Arm Node
Servo motor 4 - Gripper
Notes: Robot arm with three Degree of Freedom (3-DOF) with gripper
Four servo motors that represent the joints to enable the movement of the robotic arm
It produce a 180-degree rotation with a torque of 13 kg/cm and a turning rate at 0.14s/60 degree

## Slide 11: ARCHITECTURE
III.

## Slide 12: Architecture
NodeRed & MQTT broker
Topics
Conveyor belt
robotics/shoulderArm
robotics/baseArm
robotics/gripperArm
robotics/elbowArm
arm/controller
Publish
Subscribe
Robot Arm Node
Router & Internet
Publish
Publish
Subscribe
Subscribe
Dashboard
Operator
Smart car
robotics/wristPitchArm
robotics/wristRollArm
arm/conveyor
arm/car
car/control
car/camera
car/parameters
Notes: The architecture idealized take advantage of the local WiFi network, all the node must be properly configured to communicate each other and so that the MQTT message can be exchanged.
we have different node connected each other
we have the Robot arm node
than the camera node
thatn the detection node
the dashboard and operator
Then all the topics pass thorough the broker that manage messages of the different nodes.
The raspberryPi so is a mqtt broker and host of NodeRED system, which as we said is a flow-based graphical programming tool. where we have the control panel that control remotely the robotic arm and other panel to
stream the object through the camera and see where is positioned

## Slide 13: SOFTWARE
IV.

## Slide 14
WiFi & MQTT Connection – Robotic Arm
Notes: This is the code used to connect all the nodes in use in this architecture to the wifi and mqtt connection, so the camera node will connect to the wifi with predefined paramentes,

## Slide 15
Movement - Robotic Arm
MQTT Callback
Movement
Notes: then the detection nodes after the inizialization it will enter in loop(),
when the movement is detected,
the servo will rotates from o to 180 degree,
and calculate thought the utrasound the distance between the object and sensor and where is located thorugh the position.
Finally we publish a message to the broker.

## Slide 16
Conveyor belt
MQTT callback
Object detection & MQTT communication
Notes: then the detection nodes after the inizialization it will enter in loop(),
when the movement is detected,
the servo will rotates from o to 180 degree,
and calculate thought the utrasound the distance between the object and sensor and where is located thorugh the position.
Finally we publish a message to the broker.

## Slide 17
Movement – Smart car
MQTT Callback
Movement
Notes: then the detection nodes after the inizialization it will enter in loop(),
when the movement is detected,
the servo will rotates from o to 180 degree,
and calculate thought the utrasound the distance between the object and sensor and where is located thorugh the position.
Finally we publish a message to the broker.

## Slide 18
NodeRED
Notes: A flow-based programming tool, used to describe the purpose of each node created
It provides a browser based flow editor that makes the interconnection between nodes easy and extensible with other palette
The web page is designed to control the angle of rotation of each servomotors of the robotic arm using a control panel.
It is possible to switch from manually to automatic control.
In manual mode we can use all the slider widgets to control the robot remotely.
Publish/Subscribe mechanism is used in order to control the arm in real-time
A flow for object recognition
here we have the flow user to control the robot, to manage the detection and localization of the object and the camera
- as we can see we have three different flow with different block used to design the robot control panel
- so we can switch from manual to automatci mode
- we can use the slider widget to control the robot
- we have another flow that create the pannel to check where to pick the object
- so al this block are connectect with pub/sub mechanism in order that we can transfer message from one devide to another

## Slide 19
NodeRED
Notes: A flow-based programming tool, used to describe the purpose of each node created
It provides a browser based flow editor that makes the interconnection between nodes easy and extensible with other palette
The web page is designed to control the angle of rotation of each servomotors of the robotic arm using a control panel.
It is possible to switch from manually to automatic control.
In manual mode we can use all the slider widgets to control the robot remotely.
Publish/Subscribe mechanism is used in order to control the arm in real-time
A flow for object recognition
here we have the flow user to control the robot, to manage the detection and localization of the object and the camera
- as we can see we have three different flow with different block used to design the robot control panel
- so we can switch from manual to automatci mode
- we can use the slider widget to control the robot
- we have another flow that create the pannel to check where to pick the object
- so al this block are connectect with pub/sub mechanism in order that we can transfer message from one devide to another

## Slide 20
Robot Arm Node
Smart car
Conveyor belt
Dashboard
Node-RED + MQTT
conveyor “active”
arm/conveyor “pick”
arm/camera “take”
http request
Notes: Finally In this slide we see more in deteail how practically the messages are generated and interchanged and managed by the broker
how it comunicate with nodered
how nodeRED comunicate with the camera anche the other node.

## Slide 21
Robot Arm Node
Smart car
Conveyor belt
Dashboard
Node-RED + MQTT
arm/car “place”
arm/car “place”
arm/car “car_on”
Notes: Finally In this slide we see more in deteail how practically the messages are generated and interchanged and managed by the broker
how it comunicate with nodered
how nodeRED comunicate with the camera anche the other node.

## Slide 22
Robot Arm Node
Smart car
Conveyor belt
Dashboard
Node-RED + MQTT
car/object “the_qr_code”
conveyor “active”
Notes: Finally In this slide we see more in deteail how practically the messages are generated and interchanged and managed by the broker
how it comunicate with nodered
how nodeRED comunicate with the camera anche the other node.

## Slide 23
Robot Arm Node
Publish in:
-conveyor “active”
Camera Node
Subscribe In:
- radar/conveyor
Conveyor belt
Dashboard
Subscribe in:
- robotics/baseArm
- robotics/shoulderArm
- robotics/elbowArm
- robotics/gripperArm
- robotics/controller
- robotics/autoPickPlace
Publish in:
- camera/capture
Publish in:
- camera/capture
HTTP Request/Response
Publish in:
- robotics/baseArm
- robotics/shoulderArm
- robotics/elbowArm
- robotics/gripperArm
- robotics/controller
- robotics/autoPickPlace
Node-RED + MQTT
Publish in:
-arm/conveyor “pick”
- robotics/baseArm
- robotics/shoulderArm
- robotics/elbowArm
- robotics/gripperArm
- robotics/controller
- robotics/autoPickPlace
Notes: Finally In this slide we see more in deteail how practically the messages are generated and interchanged and managed by the broker
how it comunicate with nodered
how nodeRED comunicate with the camera anche the other node.

## Slide 24: DEMO
V.

## Slide 25
Demo

## Slide 26: Conclusions
Integrate a qr scanner to add products in the warehouse database
Upgrade the camera with a more professional one.
Upgrade the robotic arm with a professional one.
Integrate the robotic arm with a camera to track the package
Add a delivery mechanism like a drone

## Slide 27: THANK YOU
Presented by
Gerardo Martino
Computer Science – Internet of Things